## Slide 1: An Introduction to Spectroscopy & Spectrographs
Elyar Sedaghati
ESO Chile

## Slide 2: The purposes of spectroscopy
  To measure accurate wavelengths of emission and absorption lines
    Radial velocities, red shifts, etc…
  To measure relative strengths and/or EW of those lines
    Abundances, temperatures, etc…
  To measure shapes of those lines
    Density, pressure, rotation, B-fields
  To measure SED of the continuum radiation
    Physical mechanisms, temperature
Spectroscopy enables astrophysics!!

## Slide 3: How to achieve dispersion of light
  Prism (rarely used, except as cross-dispersor)
  Single-slit or grating of slits
  Transmission grating
  Grism (grating on a prism)
  Volume Phase Holographic grating
  Reflection grating
Spectroscopy enables astrophysics!!

## Slide 4: Single slit diffraction (Huygens’ principle)
Laser through a single pinhole
Angle of 1st zero intensity

## Slide 5: Multiple slit interference
b: slit width g: period α: diffraction angle β: angle of incidence

## Slide 6: Multiple slit interference & diffraction grating
  Superposition of diffraction and interference
  Pattern the same for each wavelength, but spacing changes, hence dispersion.
  Gratings generate multiple dispersion orders of increasing dispersion

## Slide 7: Multiple slit interference & diffraction grating

## Slide 8: Diffraction Gratings

## Slide 9: The diffraction grating (reflection)
  The “zeroth-order” is of no use, since it does not provide any dispersion with wavelength.
  Gratings are designed to deflect light away from this zeroth order. The further away it is deflected, the higher dispersion is achieved.
  This is done by blazing the grating, which achieves to shift the peak of grating efficiency towards higher orders.
  This also allows for the whole surface to be reflecting (as compared to slits or reflecting surfaces), which means higher throughout.
  But if a grating is blazed to be efficient at a particular wavelength with m=1, then it is also efficient at half that wavelength with m=2, so order overlap will occur!!

## Slide 10: HARPS echelle grating

## Slide 11: Overlap problem? Solution: Cross-dispersion

## Slide 12: The diffraction grating (transmission)
  Gratings also work through transmission, which come in different flavours:
  Simple transmission diffraction grating
  Grisms: add a prism to the transmission grating for zero-deviation dispersion
  Volume Phase Holographic gratings (VPH): they use modulations of the refractive index to achieve dispersion. They have very high efficiency!!

## Slide 13: Examples
  Cross-dispersed echelle spectrographs:
    HARPS+NIRPS (3p6)
    ESPRESSO (VLT/UT)
    UVES (VLT/UT2)
  Transmission grating spectrographs:
    FORS2 (VLT/UT1) – Grism + VPH
    EFOSC (NTT) – Grism
    MUSE (VLT/UT4) -- VPH

## Slide 14: Spectrographs

## Slide 15: Spectrographs
A spectrograph is a camera coupled with a dispersing element.
  By geometry
    Long-slit or multi-slit
    Single or multi-fiber
    Integral Field Units (IFU): lenslets or fiber bundles

## Slide 16: Single Object Spectrographs
Long-slit + grism/VPH
FORS2
EFOSC2
Long-slit + echelle grating
Fiber + echelle grating
UVES
ESPRESSO, HARPS+NIRPS

## Slide 17: Multi-Object Spectrographs
Multi-slit + grism/VPH
Multi-fiber + grism/VPH
FLAMES/MEDUSA (VLT/UT2) 4MOST MOONS

## Slide 18: Integral Field Spectrographs
FLAMES/ARGUS-IFU (VLT/UT2) MUSE (VLT/UT4)
KMOS (VLT/UT1)

## Slide 19: Spectral Properties

## Slide 20: From Dispersion to Resolution
The Rayleigh criterion…
Two wavelengths and are barely separable in order m if the main intensity maximum of is located at the minimum of .
Spectral Resolution: is the minimum wavelength difference that the spectrograph care reliably separate. Typically expressed in nm or .
Resolving power (): is a dimensionless quantity representing the ratio of wavelength to the spectral resolution (/ )

## Slide 21: Resolving power in practice

## Slide 22: The role of the detector
Nyquist Criterion:
In order to properly recover (sample) the
spectrograph line profile, an absolute minimum of 2 samples (pixels) per resolution element are required. While 2 pixels per FWHM of LSF is the critical sampling, 2.5 – 4.0 pixels per resolution element are desired for reliable inference of various physical parameters. The limitation here is physical restrictions on the availability of small enough pixels and opto-mech. constraints.

## Slide 23: Signal-to-Noise ratio (S/N)

## Slide 24: Signal-to-Noise ratio (S/N)

## Slide 25: Signal-to-Noise ratio (S/N)

## Slide 26: Quality of a Spectrum
  S/N, Resolving Power and Sampling are the main three parameters defining spectral quality:
    S/N depends on the brightness of the source, sky, telescope aperture size, etc…
    Resolving power is a characteristic of the dispersing element
    Sampling depends on the pixel size of the detector & the spectral resolution
  These together determine the uncertainty with which features can be measured.
  Optimal or over-sampling must be maintained. Higher sampling decreases S/N per pixel, but fitting more points will compensate for this.
  Same goes for S/N and resolution.
  Be mindful of line blending!!!

## Slide 27: Atmospheric Dispersion
  Differential atmospheric dispersion causes chromatic distortion of images that gets larger at blue wavelengths at fixed airmass and larger with airmass at a fixed central wavelength
Two solutions: 1) align slit along the parallactic angle 2) Build an Atmospheric Dispersion Corrector (ADC)

## Slide 28
@ESOAstronomy
@esoastronomy
@ESO
european-southern-observatory
@ESOobservatory
Elyar Sedaghati
esedagha@eso.org