## Slide 1: SOXS (Son Of Xshooter)
The two sides of NTT (plus ULTRACAM and AstraLux)
EFOSC2
ESO Faint Object Spectrograph &
Camera 2

## Slide 2
EFOSC2
ESO Faint Object Spectrograph &
Camera 2

## Slide 3: EFOSC2 brief timeline
      Starts operations at NTT in 11/05 1989, moved to the 2.2m telescope in 1990;
      Moved to the 3.6m in 1997, replacing EFOSC1
      Moved in 2008 to NTT to replace the ESO Multi
      Mode Instrument (EMMI)
      Lost the MOS mode in 2023
      1000+ papers so far, highest normalized citation
      count: 232 (source: ADS service)
Buzzoni et al. 1984, ESO Messenger 38, 9 .

## Slide 4: EFOSC2 in a nutshell
https://www.eso.org/sci/facilities/lasilla/instruments/efosc/inst.html
      Broad band spectroimager 350-1100 nm
      <R> ~1000
      Imaging with broad and narrow band filters (filters.ls.eso.org) (FOV:4.1’x 4.1’)
      Imaging and spectroscopic polarimetric modes available
FOCAL REDUCER
Notes: f/11 NTT  canera  f/4.9 in the CCD; pixel size (unbinned)=0.12” Basically EFOSC2 is what is familiarly called a “workhorse” instrument, i.e. an instrument with multiple capabilities and able to support many science cases.

## Slide 5: EFOSC2 in a nutshell
      CCD detector, 2048 x 2048 pixels, UV flooded
      Broad and narrow band imaging filters
      0.5” to 5” slits for spectroscopy;
      many grisms
Notes: UV flooding is a technique used to significantly increase the quantum efficiency (QE) of back-thinned, backside-illuminated CCD sensors, particularly for detecting Ultraviolet (UV) and blue light. It involves exposing the CCD's backside surface to intense UV light, often in the presence of oxygen, to charge the surface negatively. It boosts UV and blue sensitivity by creating an accumulation layer of positive charge in the native oxide layer on the back surface, which directs photoelectrons toward the charge-collecting pixel wells
.Mechanism: UV photons generate electrons that become trapped in the oxide, creating a negative potential that mitigates surface trapping effects, thus improving QE.

## Slide 6: Observing with EFOSC2 (and with any other instrument…)
https://www.eso.org/sci/facilities/lasilla/instruments/efosc/inst.html
      READ the User Manual: https://www.eso.org/sci/facilities/lasilla/instruments/efosc/doc.html
      Choose the instrument set-up: https://www.ls.eso.org/sci/facilities/lasilla/sciops/bin/efosc1.cgi and submit it the day before your observations
      Use the Exposure Time Calculator to estimate your exposure times: https://www.eso.org/observing/etc/
Notes: f/11 NTT  canera  f/4.9 in the CCD; pixel size (unbinned)=0.12” Basically EFOSC2 is what is familiarly called a “workhorse” instrument, i.e. an instrument with multiple capabilities and able to support many science cases.

## Slide 7: EFOSC2: how to observe, a.k.a. phase 2
https://www.eso.org/sci/facilities/lasilla/instruments/efosc/inst.html
https://www.eso.org/p2ls
Preparation of the observations using a dedicated web interface (p2ls): Observing Blocks (OBs) creation.
The Broker of Observing Blocks (BOB) fetches the OBs from p2ls and, by running them, sends instructions of presetting the telescope to the desired position and to set-up the instrument with the requested elements (NTT AO; overheads)
Once everything is set, the integrations are
running
Notes: Visitor mode only; raw data to the archive; pipeline at the Observatory meant for quick look only but it can be used to reduce science data when using the correct calibration frames

## Slide 8: EFOSC acquisitions

## Slide 9: EFOSC science

## Slide 10: EFOSC2 observations: the data (flow)
https://www.eso.org/sci/facilities/lasilla/instruments/efosc/inst.html
Raw data to:
archive.eso.org
INStrument workstation
Raw data
Data
Handling
System
Raw data to:
Pipeline machine
Notes: Visitor mode only; raw data to the archive; pipeline at the Observatory meant for quick look only but it can be used to reduce science data when using the correct calibration frames. When the reduced data are science ready (NIRPS/HARPS), they are also sent to the archive.

## Slide 11
@ESOAstronomy
@esoastronomy
@ESO
european-southern-observatory
@ESOobservatory
Emanuela Pompei
epompei@eso.org
Gaspare Lo Curto
glocurto@eso.org