## Slide 1
The 3.6m telescope in La Silla
and its jewels:
HARPS & NIRPS
the quest for other worlds
Emanuela Pompei
Gaspare Lo Curto

## Slide 2: A bit of History
First binary orbit reconstructed in 1889 by Vogel for the star Algol.

## Slide 3: HARPS & NIRPS: how do they detect planets ?
Radial velocity
measured via
Doppler effect

## Slide 4: Basics of HARPS & NIRPS high resolution spectrographs
Wavelength coverage | 971nm – 1854nm
Spectral resolution | 82000(HAM) / 75000(HEM)
Light feed | Fiber optics x 2 Adaptive Optics assisted
Aperture on sky | 0.4” (HAM), 0.9” (HEM)
Detector | Hawaii 4RG, 4K x 4K, 15µm pixels
Environment | Vacuum (<10-5 mbars) Cryogenic (K)
Observing modes | Simultaneous reference / Simultaneous sky
Wavelength coverage | 971nm – 1854nm
Spectral resolution | 82000(HAM) / 75000(HEM)
Light feed | Fiber optics x 2 Adaptive Optics assisted
Aperture on sky | 0.4” (HAM), 0.9” (HEM)
Detector | Hawaii 4RG, 4K x 4K, 15µm pixels
Environment | 
Observing modes | Simultaneous reference / Simultaneous sky
Wavelength coverage | 380nm – 690nm
Spectral resolution | 115000 (HAM) / 80000 (EGGS)
Light feed | Fiber optics x 2
Aperture on sky | 1” (HAM), 1.4” (EGGS)
Detector | 2 x E2V, 2K x 4K, 15µm pixels
Environment | Vacuum (<10-5 mbars) Ambient (K)
Observing modes | Simultaneous reference / Simultaneous sky / Polarimetry
Wavelength coverage | 380nm – 690nm
Spectral resolution | 115000 (HAM) / 80000 (EGGS)
Light feed | Fiber optics x 2
Aperture on sky | 1” (HAM), 1.4” (EGGS)
Detector | 2 x E2V, 2K x 4K, 15µm pixels
Environment | 
Observing modes | Simultaneous reference / Simultaneous sky / Polarimetry
HARPS
NIRPS

## Slide 5: HARPS & NIRPS Inherit from a rich past
CORAVEL
250m/s
ELODIE
10m/s
CORALIE
5m/s
HARPS
1m/s
2003
1998
1993
1981

## Slide 6
Nobel prize
in Physics
2019

## Slide 7: Planets detections (RV only)
Moore’s law for
Exo-planets ?
Flattening ?
There is more
than just the planet…
?

## Slide 8: The “planetary signature” ...
Jupiter @ 5 AU : 12.7 m s-1
Super-Earth (5 M) @ .1 AU : 1.4 m s-1
Super-Earth (5 M) @ 1 AU : 0.45 m s-1
Earth @ 1 AU : 9 cm s-1
The inclination angle “i”
is unknown => only the
minimum mass can be
determined
It is easier to detect planets
around colder, smaller stars
Orbiting a
Solar-type
star
Motivation for a NIR
planet searcher

## Slide 9: Constraints on spectrograph design
Metrological stability
Planet | Mass (MJup) | K (m/s) | HARPS/NIRPS shift (nm) | ESPRESSO shift (nm)
Mercury | 1.74 x 10-4 | 0.008 | 0.14 | 0.25
Venus | 2.56 x 10-3 | 0.086 | 1.6 | 2.7
Earth | 3.15 x 10-3 | 0.089 | 1.6 | 2.8
Mars | 3.38 x 10-4 | 0.008 | 0.14 | 0.25
Jupiter | 1.0 | 12.4 | 227 | 388
Saturn | 0.299 | 2.75 | 50 | 86
Uranus | 0.046 | 0.297 | 5.4 | 9.3
Neptune | 0.054 | 0.281 | 5.1 | 8.8
HARPS/NIRPS requirem. |  | 1 | 18 | 31
ESPRESSO requirement |  | 0.1 | 1.8 | 3.1
Silicon lattice constant: 0.54nm

## Slide 10: Constraints on spectrograph design
Spectral resolution:
R = / =
2*tan(blaze)*beam/(slit”*M1)

## Slide 11: Constraints on spectrograph design
Spectral resolution:
R = / =
2*tan(blaze)*beam/(slit”*M1)
HARPS grating: Al, R4, 20cm x 80cm
NIRPS grating: Au, R4, 9cm x 32cm
“Small” beam size thanks to A.O.

## Slide 12: Constraints on spectrograph design
Photon noise limit:
Bouchy et al., 2001

## Slide 13: Metrological stability I: spectrograph
No moving parts inside the spectrograph
Stability of the index of refraction  Instrument under vacuum (<10-3 mbar)
Strict temperature control (grating RMS <1mK / day)

## Slide 14: Metrological stability II: light injection
Variations of light distribution at the entrance slit 
variation in the lines shapes & positions
Use fiber optics to increase stability of the light injection
Fiber optics are good “scramblers” in the near field,
Not so in the far field.
Use a “Double scrambler” at spectrograph’ entrance
to exchange the near & far field.

## Slide 15: Guiding (without octagonal fibers)
“Good” guiding, 0.1” RMS,
~30 cm/s contribution to RV
“Bad” guiding, 0.5” de-centering,
~3 m/s contribution to RV
Bad centering
Fiber entrance Fiber exit
Fiber entrance Fiber exit
Good centering

## Slide 16: Octogonal fibers (near field)
Centered
De-centered
Centered (section)
De-centered (section)
From G. Avila
De-centering errors are within photon noise after double scrambler and octogonal fibers.

## Slide 17: Metrological stability III: Detector Thermal stability
CCDs thermal expansion
makes the lines move in
pixel space, i.e. simulates
a RV effect, that could in
principle be corrected by
simultaneous calibration.
Nov. 2023
Maintenance
mission
2003
2023

## Slide 18: Metrological stability IV: track the unavoidable
Instrument variations are unavoidable…
… track them !
Simultaneous calibration
Absorption cells
The HARPS experience:
the instrument drift is generally
less than 0.5m/s overnight.
the RMS of the temperature is
less than 1mK in 24 hours
a 1m/s RV drift was measured
simultaneously to a 7mK
temperature variation at the echelle
Fabry-Perot /
HC lamp

## Slide 19: Constraints on spectrograph design
Technology:
  Gratings: groove density, quality, dimension, available blaze angles;
  Detectors: detector noise, efficiency, pixel size;
  Fibers: transmission and scrambling properties
  Calibration sources: ThAr, Fabry-Perot, LFCs.

## Slide 20: Daily Calibrations
Bias
Spectroscopic flat field (localization / blaze)
Wavelength calibrations
  ThAr hollow cathode lamps
  Fabry-Perot etalon
  Laser Frequency Comb (LFC)

## Slide 21: Wavelength calibration
Associate pixels to wavelengths.
Use lines atlas (e.g. Palmer & Englmann, 1983 / Redman 2014).
Associate patterns in the spectrum with the line list.
5000.2463 ThI
5002.0972 ThI
5002.8933 ThI
5003.5981 ThI
5004.1279 ThI
5005.9752 ThI
5008.1897 ThII
5009.3344 ArII
5009.9367 ThI
5010.4174 ThI
5011.4774 ThI
5012.2754 ThI
5013.1647 Th

## Slide 22: Hollow cathod lamps (ThAr)

## Slide 23: Limitation of traditional calibrators
Lines randomly spaced  wavelength range not uniformly sampled
Lines intensities highly variable  reduction of the photon noise of the calibration
Lines have variable width  line profile variations

## Slide 24: The “ideal calibrator”
Many lines, equally spaced
Line intensities can be regulated to increase dynamical range and decrease photon noise
Lines are not resolved  the instrumental line profile is directly measurable.

## Slide 25
Laser Frequency Combs
LFC lines equation

## Slide 26: Laser Frequency Comb
Noise in the LFC data is
statistical only down to
below 2.5 cm/s !!!
(Wilken et al., Nature, 2012)
LFC on HARPS

## Slide 27: Laser Frequency Comb
LFC on NIRPS

## Slide 28: Fabry-Perot

## Slide 29: Basics of HARPS & NIRPS high resolution spectrographs
Wavelength coverage | 971nm – 1854nm
Spectral resolution | 82000(HAM) / 75000(HEM)
Light feed | Fiber optics x 2 Adaptive Optics assisted
Aperture on sky | 0.4” (HAM), 0.9” (HEM)
Detector | Hawaii 4RG, 4K x 4K, 15µm pixels
Environment | Vacuum (<10-5 mbars) Cryogenic (K)
Observing modes | Simultaneous reference / Simultaneous sky
Wavelength coverage | 971nm – 1854nm
Spectral resolution | 82000(HAM) / 75000(HEM)
Light feed | Fiber optics x 2 Adaptive Optics assisted
Aperture on sky | 0.4” (HAM), 0.9” (HEM)
Detector | Hawaii 4RG, 4K x 4K, 15µm pixels
Environment | 
Observing modes | Simultaneous reference / Simultaneous sky
Wavelength coverage | 380nm – 690nm
Spectral resolution | 115000 (HAM) / 80000 (EGGS)
Light feed | Fiber optics x 2
Aperture on sky | 1” (HAM), 1.4” (EGGS)
Detector | 2 x E2V, 2K x 4K, 15µm pixels
Environment | Vacuum (<10-5 mbars) Ambient (K)
Observing modes | Simultaneous reference / Simultaneous sky / Polarimetry
Wavelength coverage | 380nm – 690nm
Spectral resolution | 115000 (HAM) / 80000 (EGGS)
Light feed | Fiber optics x 2
Aperture on sky | 1” (HAM), 1.4” (EGGS)
Detector | 2 x E2V, 2K x 4K, 15µm pixels
Environment | 
Observing modes | Simultaneous reference / Simultaneous sky / Polarimetry
HARPS
NIRPS

## Slide 30: Basics of HARPS & NIRPS high resolution spectrographs
HARPS
NIRPS
Up-the-ramp sampling: counts per second
5.573s/sample
CCD: total number of counts

## Slide 31: Modal noise
Optical fibers are wave-guides,
the number of propagating modes depends on
the ratio of the fiber core to the wavelength.
In the IR there are much less modes,
and “modal noise” (interference between the modes)
plays an important role.
This is why NIRPS (but not HARPS) has a fiber-stretcher to “scramble” the modes and
reduce the measurable effect of the modal noise.
By Yolanda Frensch

## Slide 32: Pipeline
The same pipeline supports:
HARPS, HARPS-N, SOPHIE, CORALIE, ESPRESSO, NIRPS
with optimized instrument-dependent configuration files.
NIRPS only:
Added telluric corrections
OH subtraction

## Slide 33: Pipeline
Wavelength

## Slide 34: Operations
Very smooth operation strategy
NIRPS & HARPS can be operated either together, or individually.
NIRPS acquisition is always performed with the support of adaptive optics.
An image quality of up to 0.1” is routinely obtained in the acquisition camera.
HARPS centering and guiding is preliminary to the start of NIRPS acquisition.
Both instrument pipelines are running at the telescope and are distributed to users

## Slide 35: HARPS acquisition

## Slide 36: HARPS SCIENCE

## Slide 37: HARPS OB

## Slide 38: NIRPS + HARPS ACQUISITION

## Slide 39: NIRPS + HARPS SCIENCE

## Slide 40: NIRPS + HARPS OB

## Slide 41: NIRPS Operation panels
BOB
OS
Center
& guide
Adaptive Optics

## Slide 42: NIRPS AO panel

## Slide 43: Final remarks
Both instruments are at the top of their rank,
inherit an experience several decades long,
and are the product of continuous innovation.
The ensemble HARPS + NIRPS is the first Extreme-Precision RV instrument
ranging from 380nm to 1850nm.
HARPS is the spectrograph with the longest baseline for LFC calibrations to date.
Despite the overall complexity the operation scheme is very easy.
Both instruments have online pipelines that supply final science data products.